250P: Computer Systems
Architecture
Lecture 6: Advanced Pipelines
Anton Burtsev
April, 2020

---
Multicycle Instructions

---
Effects of Multicycle Instructions
Potentially multiple writes to the register file in a cycle
Frequent RAW hazards
WAW hazards (WAR hazards not possible)
Imprecise exceptions because of o-o-o instr completion
Note: Can also increase the “width” of the processor: handle
multiple instructions at the same time: for example, fetch
two instructions, read registers for both, execute both, etc.

---
Precise Exceptions
On an exception:
must save PC of instruction where program must resume
all instructions after that PC that might be in the pipeline
must be converted to NOPs (other instructions continue
to execute and may raise exceptions of their own)
temporary program state not in memory (in other words,
registers) has to be stored in memory
potential problems if a later instruction has already
modified memory or registers
A processor that fulfils all the above conditions is said to
provide precise exceptions (useful for debugging and of
course, correctness)

---
Dealing with these Effects
Multiple writes to the register file: increase the number of
ports, stall one of the writers during ID, stall one of the
writers during WB (the stall will propagate)
WAW hazards: detect the hazard during ID and stall the
later instruction
Imprecise exceptions: buffer the results if they complete
early or save more pipeline state so that you can return to
exactly the same state that you left at

---
Slowdowns from Stalls
Perfect pipelining with no hazards  an instruction
completes every cycle (total cycles ~ num instructions)
 speedup = increase in clock speed = num pipeline stages
With hazards and stalls, some cycles (= stall time) go by
during which no instruction completes, and then the stalled
instruction completes
Total cycles = number of instructions + stall cycles
Slowdown because of stalls = 1/ (1 + stall cycles per instr)

---
Pipelining Limits
Gap between indep instrs: T + Tovh
Gap between dep instrs: T + Tovh
Gap between indep instrs:
T/3 + Tovh
Gap between dep instrs:
T + 3Tovh
A
B
C
A
B
C
Gap between indep instrs:
T/6 + Tovh
Gap between dep instrs:
T + 6Tovh
A
B
C
D
E
F
A
B
C
D
E
F
Assume that there is a dependence where the final result of the
first instruction is required before starting the second instruction

---
Thank you!