## Slide 1
Ali Shafiee
Rajeev Balasubramonian
Feifei Li
Secure DIMM: Moving ORAM Primitives Closer to Memory
Mohit Tiwari

## Slide 2
Why ORAM?
Secure DIMM, Shafiee et al., U. Utah and U. Texas
if (x < array1_size)
y = array2[ array1[x] ];
SECRETS
array1[ ]
array2[ ]
5
10
20
PHYSICAL MEMORY
Image source: gizmodo

## Slide 3
Address Leakage
Secure DIMM, Shafiee et al., U. Utah and U. Texas
Mem
Control
EXPOSED BUSES
Processor
Trusted Computing Base (TCB)

## Slide 4
Exec Summary
Secure DIMM, Shafiee et al., U. Utah and U. Texas
ORAM to prevent access pattern leakage
ORAM has 280x bandwidth overheads
Introducing: SDIMM and 2 new ORAM protocols
Offloads ORAM to DIMMs
Uses commodity memory, improves perf & energy

## Slide 5
Path ORAM
Secure DIMM, Shafiee et al., U. Utah and U. Texas
17
Leaf 17
Data
0x0
0x1
0x2
0x3
0x1
17
Stash
Step 1. Check the PosMap for 0x1.
Step 2. Read path 17 to stash.
Step 3. Select data and change its leaf.
Step 4. Write back stash to path 17.
25
PosMap
CPU
Data
0x1
25

## Slide 6
Secure DIMMs
Secure DIMM, Shafiee et al., U. Utah and U. Texas
CPU
CPU
Encrypted Bus
Unencrypted Bus
LRDIMM Buffers
Secure Buffers
Bandwidth proportional to #DIMMs
Commodity DRAM chips
No need for trust in memory vendors

## Slide 7
Independent ORAM
Secure DIMM, Shafiee et al., U. Utah and U. Texas
CPU
ORAM0
ORAM1
ORAM split into 2 subtrees
Steps:
ACCESS(addr,DATA) to ORAM0.
1
2
2. Locally perform accessORAM.
CPU sends PROBE to check.
3
CPU sends FETCH_RESULT.
New leaf ID assigned in CPU.
4
4
4. CPU broadcasts APPEND to all
SDIMMs to move the block.
High Parallelism  But Also High Latency 

## Slide 8
Split ORAM
Secure DIMM, Shafiee et al., U. Utah and U. Texas
A
B
C
D
M
SDIMM 0
SDIMM 1
A0
B0
C0
D0
M0
A1
B1
C1
D1
M1
Odd bits of Data/Meta
Even bits of Data/Meta

## Slide 9
Split ORAM Steps
Secure DIMM, Shafiee et al., U. Utah and U. Texas
1
1
Read a path to local stashes.
2. Send metadada to CPU.
2
3. Re-assemble and decide writing
order.
3
4. Send metadata back to SDIMMs.
4
5
5. Write back the path based on
the order determined by CPU.
5
0

## Slide 10
Split-Indep ORAM
Secure DIMM, Shafiee et al., U. Utah and U. Texas
Odd
Even
Odd
Even

## Slide 11
Low-Power Modes
Secure DIMM, Shafiee et al., U. Utah and U. Texas
Rank 0
Rank 1
Rank 2
Rank 3
ORAM

## Slide 12
Design Details
Secure DIMM, Shafiee et al., U. Utah and U. Texas
New DRAM commands
Boot-up protocols
Overflow rates

## Slide 13
Methodology
Secure DIMM, Shafiee et al., U. Utah and U. Texas
Traces from Simics
  1-core, in-order, 1.6 GHz
  L1-I (32KB, 2-way), L1-D (32KB, 2-way), L2 (2MB, 10-way)
  DRAM using Micron quad-rank LRDIMM parameters
SPEC 2006 Benchmarks
Traces feed into cycle-accurate memory model
  USIMM modified to support ORAM protocols
Power
  Micron power calculator for DRAM chip power
  CACTI 7.0 for memory I/O power
Various SDIMM configs

## Slide 14
Execution Time
Secure DIMM, Shafiee et al., U. Utah and U. Texas
INDEP and SPLIT reduce exec time by 20%
INDEP-SPLIT reduces exec time by 47%
Baseline: Freecursive ORAM

## Slide 15
Energy Results
Secure DIMM, Shafiee et al., U. Utah and U. Texas
Baseline: non-secure memory

## Slide 16
Conclusions
Secure DIMM, Shafiee et al., U. Utah and U. Texas
  An approach that moves ORAM control to DIMMs
  Can combine the Independent and Split protocols
  to find the best balance of latency and parallelism
  Bandwidth demands are reduced from 280x  35x
  Execution time overheads from 5.2x  2.7x
  Reduces memory energy by 2.5x
  Employs high-capacity commodity memory