## Slide 1
Lecture 14: Sequential Circuits, FSM
Today’s topics:
  Adder wrap-up
  Sequential circuits
  Finite state machines

## Slide 2
Adder Summary
Using the generate/propagate abstraction to add layers of ccts
Key: all g/p/G/P signals can be calculated based on a/b inputs
(they don’t need carry-in as inputs, so they can all be done rightaway in parallel)
First calculate g/p with 1 gate delay: gi = ai.bi ; pi = ai + bi
Then calculate G/P with up to 2 gate delays (for a block of 4 bits):
Gi = g3 + g2.p3 + g1.p2.p3 + g0.p1.p2.p3
Pi = p0.p1.p2.p3
Then calculate all the carries, including for the 16th bit, with 2
more gate delays:
C4 = G3 + (P3.G2) + (P3.P2.G1) + (P3.P2.P1.G0) + (P3.P2.P1.P0.c0)
Thus, this abstraction enables a design with a modest number of
total gates, a modest number of delays, and a modest number of
inputs per gate.

## Slide 3
Trade-Off Curve
#inputs to each gate
# sequential gates
Truth table
sum-of-products adder, (2, 264)
gp adder (3, 33)
Carry Lookahead GP adder (7, 5)
Ripple-Carry
adder (64, 2)
# sequential gates
Performance

## Slide 4
Clocks
A microprocessor is composed of many different circuits
that are operating simultaneously – if each circuit X takes in
inputs at time TIX, takes time TEX to execute the logic,
and produces outputs at time TOX, imagine the
complications in co-ordinating the tasks of every circuit
A major school of thought (used in most processors built
today): all circuits on the chip share a clock signal (a
square wave) that tells every circuit when to accept
inputs, how much time they have to execute the logic, and
when they must produce outputs

## Slide 5
Clock Terminology
Cycle time
Rising clock edge
Falling clock edge
4 GHz = clock speed = 1 = 1 .
cycle time 250 ps

## Slide 6
Sequential Circuits
Until now, circuits were combinational – when inputs change, the
outputs change after a while (time = logic delay thru circuit)
Combinational
Circuit
Inputs
Outputs
We want the clock to act like a start and stop signal – a “latch” is
a storage device that separates these circuits – it ensures that
the inputs to the circuit do not change during a clock cycle
Combinational
Circuit
Outputs
Combinational
Circuit
Combinational
Circuit
Latch
Latch
Inputs
Clock
Clock

## Slide 7
Sequential Circuits
Sequential circuit: consists
of combinational circuit and
a storage element
At the start of the clock
cycle, the rising edge
causes the “state” storage
to store some input values
This state will not change for an entire cycle (until next rising edge)
The combinational circuit has some time to accept the value
of “state” and “inputs” and produce “outputs”
Some of the outputs (for example, the value of next “state”) may feed
back (but through the latch so they’re only seen in the next cycle)
State
Combinational Cct
Clock
Inputs
Outputs
Inputs

## Slide 8
Designing a Latch
An S-R latch: set-reset latch
  When Set is high, a 1 is stored
  When Reset is high, a 0 is stored
  When both are low, the previous state is preserved (hence,
  known as a storage or memory element)
  Both are high – this set of inputs is not allowed
  Verify the above behavior!
Source: H&P textbook

## Slide 9
D Latch
Incorporates a clock
The value of the input D signal (data) is stored only when the clock
is high – the previous state is preserved when the clock is low
Source: H&P textbook

## Slide 10
D Flip Flop
Terminology:
Latch: outputs can change any time the clock is high (asserted)
Flip flop: outputs can change only on a clock edge
Two D latches in series – ensures that a value is stored only on
the falling edge of the clock
Source: H&P textbook

## Slide 11
Finite State Machine
A sequential circuit is described by a variation of a truth
table – a finite state diagram (hence, the circuit is also
called a finite state machine)
Note that state is updated only on a clock edge
Next-state
Function
Output
Function
Current
State
Clock
Inputs
Next
state
Outputs

## Slide 12
State Diagrams
Each state is shown with a circle, labeled with the state
value – the contents of the circle are the outputs
An arc represents a transition to a different state, with the
inputs indicated on the label
0
1
0
1
D = 1
D = 0
D = 0
D = 1
This is a state diagram for ___?

## Slide 13
3-Bit Counter
Consider a circuit that stores a number and increments the value on
every clock edge – on reaching the largest value, it starts again from 0
Draw the state diagram:
  How many states?
  How many inputs?

## Slide 14
3-Bit Counter
Consider a circuit that stores a number and increments the value on
every clock edge – on reaching the largest value, it starts again from 0
Draw the state diagram:
  How many states?
  How many inputs?
000
000
001
001
010
010
011
011
100
100
101
101
110
110
111
111

## Slide 15
Tackling FSM Problems
Three questions worth asking:
  What are the possible output states? Draw a
  bubble for each.
  What are inputs? What values can those inputs take?
  For each state, what do I do for each possible
  input value? Draw an arc out of every bubble for
  every input value.

## Slide 16
Traffic Light Controller
Problem description: A traffic light with only green and red; either the
North-South road has green or the East-West road has green (both
can’t be red); there are detectors on the roads to indicate if a car is
on the road; the lights are updated every 30 seconds; a light need
change only if a car is waiting on the other road
State Transition Table:
How many states?
How many inputs?
How many outputs?

## Slide 17
State Transition Table
Problem description: A traffic light with only green and red; either the
North-South road has green or the East-West road has green (both
can’t be red); there are detectors on the roads to indicate if a car is
on the road; the lights are updated every 30 seconds; a light must
change only if a car is waiting on the other road
State Transition Table:
CurrState InputEW InputNS NextState=Output
N 0 0 N
N 0 1 N
N 1 0 E
N 1 1 E
E 0 0 E
E 0 1 N
E 1 0 E
E 1 1 N

## Slide 18
State Diagram
State Transition Table:
CurrState InputEW InputNS NextState=Output
N 0 0 N
N 0 1 N
N 1 0 E
N 1 1 E
E 0 0 E
E 0 1 N
E 1 0 E
E 1 1 N
Source: H&P textbook

## Slide 19
Tackling FSM Problems
Three questions worth asking:
  What are the possible output states? Draw a
  bubble for each.
  What are inputs? What values can those inputs take?
  For each state, what do I do for each possible
  input value? Draw an arc out of every bubble for
  every input value.

## Slide 20
Example – Residential Thermostat
Two temp sensors: internal and external
If internal temp is within 1 degree of desired, don’t
change setting
If internal temp is > 1 degree higher than desired, turn
AC on; if internal temp is < 1 degree lower than
desired, turn heater on
If external temp and desired temp are within 5
degrees, disregard the internal temp, and turn both AC
and heater off

## Slide 21
Finite State Machine Table

## Slide 22
Finite State Diagram
U-H
HEAT
COOL
OFF
U-C
D-C,
D-G,
D-H
D-C,
D-G,
D-H
D-C, D-G, D-H, U-G
U-C,
U-G
U-H,
U-G
U-C
U-H
Ext temp settings:
D – desired zone
U – undesired zone
Int temp settings:
C – cold
G – goldilocks
H – hot

## Slide 23
Latch vs. Flip-Flop
Recall that we want a circuit to have stable inputs for
an entire cycle – so I want my new inputs to arrive at
the start of a cycle and be fixed for an entire cycle
A flip-flop provides the above semantics (a door that
swings open and shut at the start of a cycle)
But a flip-flop needs two back-to-back D-latches, i.e.,
more transistors, delay, power
You can reduce these overheads with just a single
D-latch (a door that is open for half a cycle) as long as
you can tolerate stable inputs for just half a cycle