## Slide 1
Lecture 20: Branches, OOO
Today’s topics:
  Branch prediction
  Out-of-order execution
  (Also see class notes on pipelining, hazards, etc.)

## Slide 2
Problem 4 – no Byp
IF
Dec
ALU
DM
RW
ALU
DM
RW
lw $1, 8($2)
add $4, $1, $3
IF
Dec
RR
A 7 or 9 stage pipeline, RR and RW take an entire stage

## Slide 3
Problem 4 – with Byp
IF
Dec
ALU
DM
RW
ALU
DM
RW
lw $1, 8($2)
add $4, $1, $3
IF
Dec
RR
A 7 or 9 stage pipeline, RR and RW take an entire stage

## Slide 4
Problem 4
IF
Dec
ALU
DM
RW
ALU
DM
RW
lw $1, 8($2)
add $4, $1, $3
IF
Dec
RR
Without bypassing: 4 stalls
IF:IF:DE:DE:RR:AL:DM:DM:RW
IF: IF :DE:DE:DE:DE: DE :DE:RR:AL:RW
With bypassing: 2 stalls
IF:IF:DE:DE:RR:AL:DM:DM:RW
IF: IF :DE:DE:DE:DE: RR :AL:RW

## Slide 5
Pipelining Example (Recap)
Unpipelined design: the entire circuit takes 10ns to finish
Cycle time = 10ns; Clock speed = 1/10ns = 100 MHz
CPI = 1 (assuming no stalls)
Throughput in instructions per second =
#cycles in a second x instructions-per-cycle =
100 M x 1 = 100 M instrs per second = 0.1 BIPS (billion instrs per sec)
5-stage pipeline: under ideal conditions, each stage takes 2ns
Cycle time = 2ns; Clock speed = 1/2ns = 500 MHz (5x higher)
CPI = 1 (continuing to assume no stalls)
Throughput = # cycles in a second x instrs-per-cycle
= 500 M x 1 = 500 MIPS = 0.5 BIPS
Under ideal conditions, a 5-stage pipeline gives a 5x speedup.

## Slide 6
Control Hazards
Simple techniques to handle control hazard stalls:
  for every branch, introduce a stall cycle (note: every
  6th instruction is a branch!)
  assume the branch is not taken and start fetching the
  next instruction – if the branch is taken, need hardware
  to cancel the effect of the wrong-path instruction
  fetch the next instruction (branch delay slot) and
  execute it anyway – if the instruction turns out to be
  on the correct path, useful work was done – if the
  instruction turns out to be on the wrong path,
  hopefully program state is not lost
  make a smarter guess and fetch instructions from the
  expected target

## Slide 7
Control Hazards
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW
IF
D/R
ALU
DM
RW

## Slide 8
Branch Delay Slots
Source: H&P textbook

## Slide 9
Pipeline without Branch Predictor
IF (br)
PC
Reg Read
Compare
Br-target
PC + 4

## Slide 10
Pipeline with Branch Predictor
IF (br)
PC
Reg Read
Compare
Br-target
Branch
Predictor

## Slide 11
Bimodal Predictor
Branch PC
14 bits
Table of
16K entries
of 2-bit
saturating
counters

## Slide 12
2-Bit Prediction
For each branch, maintain a 2-bit saturating counter:
if the branch is taken: counter = min(3,counter+1)
if the branch is not taken: counter = max(0,counter-1)
… sound familiar?
If (counter >= 2), predict taken, else predict not taken
The counter attempts to capture the common case for
each branch
Indexing functions
Multiple branch predictors
History, trade-offs

## Slide 13
Slowdowns from Stalls
Perfect pipelining with no hazards  an instruction
completes every cycle (total cycles ~ num instructions)
 speedup = increase in clock speed = num pipeline stages
With hazards and stalls, some cycles (= stall time) go by
during which no instruction completes, and then the stalled
instruction completes
Total cycles = number of instructions + stall cycles

## Slide 14
Multicycle Instructions
Multiple parallel pipelines – each pipeline can have a different
number of stages
Instructions can now complete out of order – must make sure
that writes to a register happen in the correct order