## Slide 1
Lecture: Static ILP
Topics: loop scheduling, loop unrolling, software pipelines

## Slide 2
Smart Schedule
By re-ordering instructions, it takes 6 cycles per iteration instead of 10
We were able to violate an anti-dependence easily because an
immediate was involved
Loop overhead (instrs that do book-keeping for the loop): 2
Actual work (the ld, add.d, and s.d): 3 instrs
Can we somehow get execution time to be 3 cycles per iteration?
Loop: L.D F0, 0(R1)
stall
ADD.D F4, F0, F2
stall
stall
S.D F4, 0(R1)
DADDUI R1, R1,# -8
stall
BNE R1, R2, Loop
stall
Loop: L.D F0, 0(R1)
DADDUI R1, R1,# -8
ADD.D F4, F0, F2
stall
BNE R1, R2, Loop
S.D F4, 8(R1)
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 3
Problem 1
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many cycles do the default and optimized schedules take?

## Slide 4
Problem 1
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many cycles do the default and optimized schedules take?
Unoptimized: LD 1s MUL 4s SD DA DA BNE 1s -- 12 cycles
Optimized: LD DA MUL DA 2s BNE SD -- 8 cycles

## Slide 5
Loop Unrolling
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
L.D F6, -8(R1)
ADD.D F8, F6, F2
S.D F8, -8(R1)
L.D F10,-16(R1)
ADD.D F12, F10, F2
S.D F12, -16(R1)
L.D F14, -24(R1)
ADD.D F16, F14, F2
S.D F16, -24(R1)
DADDUI R1, R1, #-32
BNE R1,R2, Loop
Loop overhead: 2 instrs; Work: 12 instrs
How long will the above schedule take to complete?

## Slide 6
Scheduled and Unrolled Loop
Loop: L.D F0, 0(R1)
L.D F6, -8(R1)
L.D F10,-16(R1)
L.D F14, -24(R1)
ADD.D F4, F0, F2
ADD.D F8, F6, F2
ADD.D F12, F10, F2
ADD.D F16, F14, F2
S.D F4, 0(R1)
S.D F8, -8(R1)
DADDUI R1, R1, # -32
S.D F12, 16(R1)
BNE R1,R2, Loop
S.D F16, 8(R1)
Execution time: 14 cycles or 3.5 cycles per original iteration
LD -> any : 1 stall
FPALU -> any: 3 stalls
FPALU -> ST : 2 stalls
IntALU -> BR : 1 stall

## Slide 7
Loop Unrolling
Increases program size
Requires more registers
To unroll an n-iteration loop by degree k, we will need (n/k)
iterations of the larger loop, followed by (n mod k) iterations
of the original loop

## Slide 8
Automating Loop Unrolling
Determine the dependences across iterations: in the
example, we knew that loads and stores in different iterations
did not conflict and could be re-ordered
Determine if unrolling will help – possible only if iterations
are independent
Determine address offsets for different loads/stores
Dependency analysis to schedule code without introducing
hazards; eliminate name dependences by using additional
registers

## Slide 9
Problem 2
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many unrolls does it take to avoid stall cycles?

## Slide 10
Problem 2
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many unrolls does it take to avoid stall cycles?
Degree 2: LD LD MUL MUL DA DA 1s SD BNE SD
Degree 3: LD LD LD MUL MUL MUL DA DA SD SD BNE SD
– 12 cyc/3 iterations

## Slide 11
Superscalar Pipelines
Integer pipeline FP pipeline
Handles L.D, S.D, ADDUI, BNE Handles ADD.D
What is the schedule with an unroll degree of 5?

## Slide 12
Superscalar Pipelines
Integer pipeline FP pipeline
Loop: L.D F0,0(R1)
L.D F6,-8(R1)
L.D F10,-16(R1) ADD.D F4,F0,F2
L.D F14,-24(R1) ADD.D F8,F6,F2
L.D F18,-32(R1) ADD.D F12,F10,F2
S.D F4,0(R1) ADD.D F16,F14,F2
S.D F8,-8(R1) ADD.D F20,F18,F2
S.D F12,-16(R1)
DADDUI R1,R1,# -40
S.D F16,16(R1)
BNE R1,R2,Loop
S.D F20,8(R1)
Need unroll by degree 5 to eliminate stalls (fewer if we move DADDUI up)
The compiler may specify instructions that can be issued as one packet
The compiler may specify a fixed number of instructions in each packet:
Very Large Instruction Word (VLIW)

## Slide 13
Problem 3
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many unrolls does it take to avoid stalls in the superscalar pipeline?

## Slide 14
Problem 3
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
How many unrolls does it take to avoid stalls in the superscalar pipeline?
LD
LD
LD MUL
LD MUL
LD MUL 7 unrolls. Could also make do with 5 if we
LD MUL moved up the DADDUIs.
LD MUL
SD MUL

## Slide 15
Software Pipeline?!
L.D
ADD.D
S.D
DADDUI
BNE
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
L.D
ADD.D
DADDUI
BNE
DADDUI
BNE
DADDUI
BNE
DADDUI
BNE
DADDUI
BNE
…
…
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop

## Slide 16
Software Pipeline
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
S.D
L.D
ADD.D
L.D
Original iter 1
Original iter 2
Original iter 3
Original iter 4
New iter 1
New iter 2
New iter 3
New iter 4

## Slide 17
Software Pipelining
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
Loop: S.D F4, 16(R1)
ADD.D F4, F0, F2
L.D F0, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
Advantages: achieves nearly the same effect as loop unrolling, but
without the code expansion – an unrolled loop may have inefficiencies
at the start and end of each iteration, while a sw-pipelined loop is
almost always in steady state – a sw-pipelined loop can also be unrolled
to reduce loop overhead
Disadvantages: does not reduce loop overhead, may require more
registers

## Slide 18
Recall Superscalar Pipeline Example
Integer pipeline FP pipeline
Loop: L.D F0,0(R1)
L.D F6,-8(R1)
L.D F10,-16(R1) ADD.D F4,F0,F2
L.D F14,-24(R1) ADD.D F8,F6,F2
L.D F18,-32(R1) ADD.D F12,F10,F2
S.D F4,0(R1) ADD.D F16,F14,F2
S.D F8,-8(R1) ADD.D F20,F18,F2
S.D F12,-16(R1)
DADDUI R1,R1,# -40
S.D F16,16(R1)
BNE R1,R2,Loop
S.D F20,8(R1)
Need unroll by degree 5 to eliminate stalls (fewer if we move DADDUI up)
The compiler may specify instructions that can be issued as one packet
The compiler may specify a fixed number of instructions in each packet:
Very Large Instruction Word (VLIW)

## Slide 19
Problem 4
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
Show the SW pipelined version of the code and does it cause stalls?

## Slide 20
Problem 4
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
Show the SW pipelined version of the code and does it cause stalls?
Loop: S.D F4, 0(R2)
MUL F4, F0, F2
L.D F0, 0(R1)
DADDUI R2, R2, #-8
BNE R1, R3, Loop
DADDUI R1, R1, #-8 There will be no stalls