## Slide 1
Lecture: Branch Prediction, Out-of-order Processors
Topics: branch predictors, out-of-order intro, register renaming

## Slide 2
2-Bit Bimodal Prediction
For each branch, maintain a 2-bit saturating counter:
if the branch is taken: counter = min(3,counter+1)
if the branch is not taken: counter = max(0,counter-1)
If (counter >= 2), predict taken, else predict not taken
Advantage: a few atypical branches will not influence the
prediction (a better measure of “the common case”)
Especially useful when multiple branches share the same
counter (some bits of the branch PC are used to index
into the branch predictor)
Can be easily extended to N-bits (in most processors, N=2)

## Slide 3
Bimodal 2-Bit Predictor
Branch PC
10 bits
Table of
1K entries
Each
entry is
a 2-bit
sat.
counter
The table keeps track of the common-case
outcome for the branch

## Slide 4
Correlating Predictors
Basic branch prediction: maintain a 2-bit saturating
counter for each entry (or use 10 branch PC bits to index
into one of 1024 counters) – captures the recent
“common case” for each branch
Can we take advantage of additional information?
  If a branch recently went 01111, expect 0; if it
  recently went 11101, expect 1; can we have a
  separate counter for each case?
  If the previous branches went 01, expect 0; if the
  previous branches went 11, expect 1; can we have
  a separate counter for each case?
  Hence, build correlating predictors

## Slide 5
Global Predictor
Branch PC
10 bits
Table of
16K entries
Each
entry is
a 2-bit
sat.
counter
The table keeps track of the common-case
outcome for the branch/history combo
Global history
CAT or XOR

## Slide 6
Local Predictor
Branch PC
Table of
16K entries
of 2-bit
saturating
counters
Table of 64 entries of 14-bit
histories for a single branch
10110111011001
Use 6 bits of branch PC to
index into local history table
14-bit history
indexes into
next level
Also a two-level predictor that only
uses local histories at the first level

## Slide 7
Local Predictor
Branch PC
6 bits
Table of
1K entries
Each
entry is
a 2-bit
sat.
counter
The table keeps track of the common-case
outcome for the branch/local-history combo
Local history
10 bit entries
XOR
64 entries
10 bits

## Slide 8
Local/Global Predictors
Instead of maintaining a counter for each branch to
capture the common case,
Maintain a counter for each branch and surrounding pattern
If the surrounding pattern belongs to the branch being
predicted, the predictor is referred to as a local predictor
If the surrounding pattern includes neighboring branches,
the predictor is referred to as a global predictor

## Slide 9
Tournament Predictors
A local predictor might work well for some branches or
programs, while a global predictor might work well for others
Provide one of each and maintain another predictor to
identify which predictor is best for each branch
Tournament
Predictor
Branch PC
Table of 2-bit
saturating counters
Local
Predictor
Global
Predictor
M
U
X
Alpha 21264:
1K entries in level-1
1K entries in level-2
4K entries
12-bit global history
4K entries
Total capacity: ?

## Slide 10
Branch Target Prediction
In addition to predicting the branch direction, we must
also predict the branch target address
Branch PC indexes into a predictor table; indirect branches
might be problematic
Most common indirect branch: return from a procedure –
can be easily handled with a stack of return addresses

## Slide 11
Problem 1
What is the storage requirement for a global predictor
that uses 3-bit saturating counters and that produces
an index by XOR-ing 12 bits of branch PC with 12 bits
of global history?

## Slide 12
Problem 1
What is the storage requirement for a global predictor
that uses 3-bit saturating counters and that produces
an index by XOR-ing 12 bits of branch PC with 12 bits
of global history?
The index is 12 bits wide, so the table has 2^12 saturating
counters. Each counter is 3 bits wide. So total storage
= 3 * 4096 = 12 Kb or 1.5 KB

## Slide 13
Problem 2
What is the storage requirement for a tournament predictor
that uses the following structures:
  a “selector” that has 4K entries and 2-bit counters
  a “global” predictor that XORs 14 bits of branch PC
  with 14 bits of global history and uses 3-bit counters
  a “local” predictor that uses an 8-bit index into L1, and
  produces a 12-bit index into L2 by XOR-ing branch PC
  and local history. The L2 uses 2-bit counters.

## Slide 14
Problem 2
What is the storage requirement for a tournament predictor
that uses the following structures:
  a “selector” that has 4K entries and 2-bit counters
  a “global” predictor that XORs 14 bits of branch PC
  with 14 bits of global history and uses 3-bit counters
  a “local” predictor that uses an 8-bit index into L1, and
  produces a 12-bit index into L2 by XOR-ing branch PC
  and local history. The L2 uses 2-bit counters.
  Selector = 4K * 2b = 8 Kb
  Global = 3b * 2^14 = 48 Kb
  Local = (12b * 2^8) + (2b * 2^12) = 3 Kb + 8 Kb = 11 Kb
  Total = 67 Kb

## Slide 15
Problem 3
For the code snippet below, estimate the steady-state
bpred accuracies for the default PC+4 prediction, the
1-bit bimodal, 2-bit bimodal, global, and local predictors.
Assume that the global/local preds use 5-bit histories.
do {
for (i=0; i<4; i++) {
increment something
}
for (j=0; j<8; j++) {
increment something
}
k++;
} while (k < some large number)

## Slide 16
Problem 3
For the code snippet below, estimate the steady-state
bpred accuracies for the default PC+4 prediction, the
1-bit bimodal, 2-bit bimodal, global, and local predictors.
Assume that the global/local preds use 5-bit histories.
do {
for (i=0; i<4; i++) {
increment something
}
for (j=0; j<8; j++) {
increment something
}
k++;
} while (k < some large number)
PC+4: 2/13 = 15%
1b Bim: (2+6+1)/(4+8+1)
= 9/13 = 69%
2b Bim: (3+7+1)/13
= 11/13 = 85%
Global: (4+7+1)/13
= 12/13 = 92%
Local: (4+7+1)/13
= 12/13 = 92%

## Slide 17
An Out-of-Order Processor Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
T1
T2
T3
T4
T5
T6
Reorder Buffer (ROB)
T1  R1+R2
T2  T1+R3
BEQZ T2
T4  T1+T2
T5  T4+T2
Issue Queue (IQ)
ALU
ALU
ALU
Register File
R1-R32
Results written to
ROB and tags
broadcast to IQ

## Slide 18
Problem 1
Show the renamed version of the following code:
Assume that you have 4 rename registers T1-T4
R1  R2+R3
R3  R4+R5
BEQZ R1
R1  R1 + R3
R1  R1 + R3
R3  R1 + R3

## Slide 19
Problem 1
Show the renamed version of the following code:
Assume that you have 4 rename registers T1-T4
R1  R2+R3 T1  R2+R3
R3  R4+R5 T2  R4+R5
BEQZ R1 BEQZ T1
R1  R1 + R3 T4  T1+T2
R1  R1 + R3 T1  T4+T2
R3  R1 + R3 T2  T1 +R3

## Slide 20
Design Details - I
Instructions enter the pipeline in order
No need for branch delay slots if prediction happens in time
Instructions leave the pipeline in order – all instructions
that enter also get placed in the ROB – the process of an
instruction leaving the ROB (in order) is called commit –
an instruction commits only if it and all instructions before
it have completed successfully (without an exception)
To preserve precise exceptions, a result is written into the
register file only when the instruction commits – until then,
the result is saved in a temporary register in the ROB

## Slide 21
Design Details - II
Instructions get renamed and placed in the issue queue –
some operands are available (T1-T6; R1-R32), while
others are being produced by instructions in flight (T1-T6)
As instructions finish, they write results into the ROB (T1-T6)
and broadcast the operand tag (T1-T6) to the issue queue –
instructions now know if their operands are ready
When a ready instruction issues, it reads its operands from
T1-T6 and R1-R32 and executes (out-of-order execution)
Can you have WAW or WAR hazards? By using more
names (T1-T6), name dependences can be avoided

## Slide 22
Design Details - III
If instr-3 raises an exception, wait until it reaches the top
of the ROB – at this point, R1-R32 contain results for all
instructions up to instr-3 – save registers, save PC of instr-3,
and service the exception
If branch is a mispredict, flush all instructions after the
branch and start on the correct path – mispredicted instrs
will not have updated registers (the branch cannot commit
until it has completed and the flush happens as soon as the
branch completes)
Potential problems: ?