## Slide 1
Lecture: Virtual Memory
Topics: virtual memory details, TLB/cache access, superpages

## Slide 2
Core 0
L1
D$
L1
I$
L2 $
Core 1
L1
D$
L1
I$
L2 $
Core 2
L1
D$
L1
I$
L2 $
Core 3
L1
D$
L1
I$
L2 $
Core 4
L1
D$
L1
I$
L2 $
Core 5
L1
D$
L1
I$
L2 $
Core 6
L1
D$
L1
I$
L2 $
Core 7
L1
D$
L1
I$
L2 $
Memory Controller for off-chip access
A single tile composed
of a core, L1 caches, and
a bank (slice) of the
shared L2 cache
The cache controller
forwards address requests
to the appropriate L2 bank
and handles coherence
operations
Shared NUCA Cache

## Slide 3
Problem 1
Assume a large shared LLC that is tiled and distributed on the chip.
Assume 16 tiles. Assume an OS page size of 8KB. The entire LLC
has a size of 32 MB, uses 64-byte blocks, and is 8-way set-associative.
Which of the 40 physical address bits are used to specify the tile number?
Provide an example page number that is assigned to tile 0.

## Slide 4
Problem 1
Assume a large shared LLC that is tiled and distributed on the chip.
Assume 16 tiles. Assume an OS page size of 8KB. The entire LLC
has a size of 32 MB, uses 64-byte blocks, and is 8-way set-associative.
Which of the 40 physical address bits are used to specify the tile number?
Provide an example page number that is assigned to tile 0.
The cache has 64K sets, i.e., 6 block offset bits, 16 index bits, and
18 tag bits. The address also has a 13-bit page offset, and 27 page
number bits. Nine bits (bits 14-22) are used for the page number and
the index bits. Any four of those bits can be used to designate the tile
number, say, bits 19-22. An example page number assigned to tile 0
is xxx…xxx0000xxx…xxx
bit 22 19
40 Tag 23
22 Index 7
6 Offset 1
40 Page number 14
13 Page offset 1

## Slide 5
Address Translation
The virtual and physical memory are broken up into pages
Virtual address
8KB page size
page offset
virtual page
number
Translated to phys
page number
Physical memory
13
Physical address
page offset
physical page
number
13

## Slide 6
TLB
Since the number of pages is very high, the page table
capacity is too large to fit on chip
A translation lookaside buffer (TLB) caches the virtual
to physical page number translation for recent accesses
A TLB miss requires us to access the page table, which
may not even be found in the cache – two expensive
memory look-ups to access one word of data!
A large page size can increase the coverage of the TLB
and reduce the capacity of the page table, but also
increases memory waste

## Slide 7
Problem 2
Build an example toy virtual memory system. Each program has 8
virtual pages. Two programs are running together. The physical
memory can store 8 total pages. Show example contents of the
physical memory, disk, page table, TLB. Assume that virtual pages
take names a-z and physical pages take names A-Z.
Processor
TLB
aA
cC
mM
zZ
Memory
A B C D
M N O Z
Disk
E’F’G’H’P’Q’
Other Files
Page table
aA mM
bB nN
cC oO
dD pP’
eE’ qQ’
fF’
gG’
hH’

## Slide 8
TLB and Cache
Is the cache indexed with virtual or physical address?
  To index with a physical address, we will have to first
  look up the TLB, then the cache  longer access time
  Multiple virtual addresses can map to the same
  physical address – can we ensure that these
  different virtual addresses will map to the same
  location in cache? Else, there will be two different
  copies of the same physical memory word
Does the tag array store virtual or physical addresses?
  Since multiple virtual addresses can map to the same
  physical address, a virtual tag comparison can flag a
  miss even if the correct physical memory word is present

## Slide 9
TLB and Cache

## Slide 10
Virtually Indexed Caches
24-bit virtual address, 4KB page size  12 bits offset and
12 bits virtual page number
To handle the example below, the cache must be designed to use only 12
index bits – for example, make the 64KB cache 16-way
Page coloring can ensure that some bits of virtual and physical address match
abcdef
abbdef
Page in physical
memory
Data cache that needs 16
index bits 64KB direct-mapped
or 128KB 2-way…
cdef
bdef
Virtually indexed
cache

## Slide 11
Cache and TLB Pipeline
TLB
Virtual address
Tag array
Data array
Physical tag comparion
Virtual page number
Virtual
index
Offset
Physical page number
Physical tag
Virtually Indexed; Physically Tagged Cache

## Slide 12
Problem 3
Assume that page size is 16KB and cache block size is 32 B.
If I want to implement a virtually indexed physically tagged
L1 cache, what is the largest direct-mapped L1 that I can
implement? What is the largest 2-way cache that I can
implement?

## Slide 13
Problem 3
Assume that page size is 16KB and cache block size is 32 B.
If I want to implement a virtually indexed physically tagged
L1 cache, what is the largest direct-mapped L1 that I can
implement? What is the largest 2-way cache that I can
implement?
There are 14 page offset bits. If 5 of them are used for
block offset, there are 9 more that I can use for index.
512 sets  16KB direct-mapped or 32KB 2-way cache

## Slide 14
Protection
The hardware and operating system must co-operate to
ensure that different processes do not modify each other’s
memory
The hardware provides special registers that can be read
in user mode, but only modified by instrs in supervisor mode
A simple solution: the physical memory is divided between
processes in contiguous chunks by the OS and the bounds
are stored in special registers – the hardware checks every
program access to ensure it is within bounds
Protection bits are tracked in the TLB on a per-page basis

## Slide 15
Superpages
If a program’s working set size is 16 MB and page size is
8KB, there are 2K frequently accessed pages – a 128-entry
TLB will not suffice
By increasing page size to 128KB, TLB misses will be
eliminated – disadvantage: memory waste, increase in
page fault penalty
Can we change page size at run-time?
Note that a single page has to be contiguous in physical
memory

## Slide 16
Superpages Implementation
At run-time, build superpages if you find that contiguous
virtual pages are being accessed at the same time
For example, virtual pages 64-79 may be frequently
accessed – coalesce these pages into a single superpage
of size 128KB that has a single entry in the TLB
The physical superpage has to be in contiguous physical
memory – the 16 physical pages have to be moved so
they are contiguous
…
virtual
physical
virtual
physical

## Slide 17
Ski Rental Problem
Promoting a series of contiguous virtual pages into a
superpage reduces TLB misses, but has a cost: copying
physical memory into contiguous locations
Page usage statistics can determine if pages are good
candidates for superpage promotion, but if cost of a TLB
miss is x and cost of copying pages is Nx, when do you
decide to form a superpage?
If ski rentals cost $50 and new skis cost $500, when do I
decide to buy new skis?
  If I rent 10 times and then buy skis, I’m guaranteed to
  not spend more than twice the optimal amount

## Slide 18
DRAM Main Memory
Main memory is stored in DRAM cells that have much
higher storage density
DRAM cells lose their state over time – must be refreshed
periodically, hence the name Dynamic
DRAM access suffers from long access time and high
energy overhead

## Slide 19
Memory Architecture
Processor
Memory Controller
Address/Cmd
Data
DIMM
Bank
Row Buffer
DIMM: a PCB with DRAM chips on the back and front
Rank: a collection of DRAM chips that work together to respond to a
request and keep the data bus full
A 64-bit data bus will need 8 x8 DRAM chips or 4 x16 DRAM chips or..
Bank: a subset of a rank that is busy during one request
Row buffer: the last row (say, 8 KB) read from a bank, acts like a cache