## Slide 1
Lecture: Coherence Protocols
Topics: multi-thread programming models,
snooping-based protocols, directory-based protocols

## Slide 2
Multiprocs -- Memory Organization - I
Centralized shared-memory multiprocessor or
Symmetric shared-memory multiprocessor (SMP)
Multiple processors connected to a single centralized
memory – since all processors see the same memory
organization  uniform memory access (UMA)
Shared-memory because all processors can access the
entire memory address space
Can centralized memory emerge as a bandwidth
bottleneck? – not if you have large caches and employ
fewer than a dozen processors

## Slide 3
SMPs or Centralized Shared-Memory
Processor
Caches
Processor
Caches
Processor
Caches
Processor
Caches
Main Memory
I/O System

## Slide 4
Multiprocs -- Memory Organization - II
For higher scalability, memory is distributed among
processors  distributed memory multiprocessors
If one processor can directly address the memory local
to another processor, the address space is shared 
distributed shared-memory (DSM) multiprocessor
If memories are strictly local, we need messages to
communicate data  cluster of computers or multicomputers
Non-uniform memory architecture (NUMA) since local
memory has lower latency than remote memory

## Slide 5
SMPs
Centralized main memory and many caches  many
copies of the same data
A system is cache coherent if a read returns the most
recently written value for that word
Time Event Value of X in Cache-A Cache-B Memory
0 - - 1
1 CPU-A reads X 1 - 1
2 CPU-B reads X 1 1 1
3 CPU-A stores 0 in X 0 1 0

## Slide 6
Cache Coherence
A memory system is coherent if:
Write propagation: P1 writes to X, sufficient time elapses,
P2 reads X and gets the value written by P1
Write serialization: Two writes to the same location by two
processors are seen in the same order by all processors
The memory consistency model defines “time elapsed”
before the effect of a processor is seen by others and the
ordering with R/W to other locations (loosely speaking
– more later)

## Slide 7
SMPs or Centralized Shared-Memory
Processor
Caches
Processor
Caches
Processor
Caches
Processor
Caches
Main Memory
I/O System

## Slide 8
Design Issues
Invalidate
Find data
Writeback / writethrough
Processor
Caches
Processor
Caches
Processor
Caches
Processor
Caches
Main Memory
I/O System
Cache block states
Contention for tags
Enforcing write serialization

## Slide 9
SMP Example
Processor
A
Caches
Processor
B
Caches
Processor
C
Caches
Processor
D
Caches
Main Memory
I/O System
A: Rd X
B: Rd X
C: Rd X
A: Wr X
A: Wr X
C: Wr X
B: Rd X
A: Rd X
A: Rd Y
B: Wr X
B: Rd Y
B: Wr X
B: Wr Y

## Slide 10
Example
P1 reads X: not found in cache-1, request sent on bus, memory responds,
X is placed in cache-1 in shared state
P2 reads X: not found in cache-2, request sent on bus, everyone snoops
this request, cache-1 does nothing because this is just a read request,
memory responds, X is placed in cache-2 in shared state
P1
Cache-1
P2
Cache-2
Main Memory
P1 writes X: cache-1 has data in shared
state (shared only provides read perms),
request sent on bus, cache-2 snoops and
then invalidates its copy of X, cache-1
moves its state to modified
P2 reads X: cache-2 has data in invalid
state, request sent on bus, cache-1 snoops
and realizes it has the only valid copy, so it
downgrades itself to shared state and
responds with data, X is placed in cache-2
in shared state, memory is also updated

## Slide 11
Example
Request | Cache Hit/Miss | Request on the bus | Who responds | State in Cache 1 | State in Cache 2 | State in Cache 3 | State in Cache 4
 |  |  |  | Inv | Inv | Inv | Inv
P1: Rd X | Miss | Rd X | Memory | S | Inv | Inv | Inv
P2: Rd X | Miss | Rd X | Memory | S | S | Inv | Inv
P2: Wr X | Perms Miss | Upgrade X | No response. Other caches invalidate. | Inv | M | Inv | Inv
P3: Wr X | Write Miss | Wr X | P2 responds | Inv | Inv | M | Inv
P3: Rd X | Read Hit | - | - | Inv | Inv | M | Inv
P4: Rd X | Read Miss | Rd X | P3 responds. Mem wrtbk | Inv | Inv | S | S

## Slide 12
Cache Coherence Protocols
Directory-based: A single location (directory) keeps track
of the sharing status of a block of memory
Snooping: Every cache block is accompanied by the sharing
status of that block – all cache controllers monitor the
shared bus so they can update the sharing status of the
block, if necessary
Write-invalidate: a processor gains exclusive access of
a block before writing by invalidating all other copies
Write-update: when a processor writes, it updates other
shared copies of that block

## Slide 13
Directory-Based Cache Coherence
The physical memory is distributed among all processors
The directory is also distributed along with the
corresponding memory
The physical address is enough to determine the location
of memory
The (many) processing nodes are connected with a
scalable interconnect (not a bus) – hence, messages
are no longer broadcast, but routed from sender to
receiver – since the processing nodes can no longer
snoop, the directory keeps track of sharing state

## Slide 14
Distributed Memory Multiprocessors
Processor
& Caches
Memory
I/O
Processor
& Caches
Memory
I/O
Processor
& Caches
Memory
I/O
Processor
& Caches
Memory
I/O
Interconnection network
Directory
Directory
Directory
Directory

## Slide 15
Directory-Based Example
Processor
& Caches
Memory
I/O
Processor
& Caches
Memory
I/O
Processor
& Caches
Memory
I/O
Interconnection network
Directory
Directory
X
Directory
Y
A: Rd X
B: Rd X
C: Rd X
A: Wr X
A: Wr X
C: Wr X
B: Rd X
A: Rd X
A: Rd Y
B: Wr X
B: Rd Y
B: Wr X
B: Wr Y

## Slide 16
Example
Request | Cache Hit/Miss | Messages | Dir State | State in C1 | State in C2 | State in C3 | State in C4
 |  |  |  | Inv | Inv | Inv | Inv
P1: Rd X | Miss | Rd-req to Dir. Dir responds. | X: S: 1 | S | Inv | Inv | Inv
P2: Rd X | Miss | Rd-req to Dir. Dir responds. | X: S: 1, 2 | S | S | Inv | Inv
P2: Wr X | Perms Miss | Upgr-req to Dir. Dir sends INV to P1. P1 sends ACK to Dir. Dir grants perms to P2. | X: M: 2 | Inv | M | Inv | Inv
P3: Wr X | Write Miss | Wr-req to Dir. Dir fwds request to P2. P2 sends data to Dir. Dir sends data to P3. | X: M: 3 | Inv | Inv | M | Inv
P3: Rd X | Read Hit | - | - | Inv | Inv | M | Inv
P4: Rd X | Read Miss | Rd-req to Dir. Dir fwds request to P3. P3 sends data to Dir. Memory wrtbk. Dir sends data to P4. | X: S: 3, 4 | Inv | Inv | S | S

## Slide 17
Cache Block States
What are the different states a block of memory can have
within the directory?
Note that we need information for each cache so that
invalidate messages can be sent
The block state is also stored in the cache for efficiency
The directory now serves as the arbitrator: if multiple
write attempts happen simultaneously, the directory
determines the ordering