250P: Computer Systems
Architecture
Lecture 4: Basics of pipelining
Anton Burtsev
April, 2021

---
View from 5,000 Feet
Source: H&P textbook

---
Latches and Clocks in a Single-Cycle Design
PC
Instr
Mem
Reg
File
ALU
Addr
Data
Memory
The entire instruction executes in a single cycle
Green blocks are latches
At the rising edge, a new PC is recorded
At the rising edge, the result of the previous cycle is recorded
At the falling edge, the address of LW/SW is recorded so
we can access the data memory in the 2nd half of the cycle

---
Multi-Stage Circuit
Instead of executing the entire instruction in a single cycle (a single stage), let’s break up the execution into multiple stages, each separated by a latch
PC
Instr
Mem
L2
Reg
File
ALU
L4
L3
Data
Memory
L5
Reg
File

---
Building a Car
Time

---
Building a Car
Unpipelined
Start and finish a job before moving to the next
Jobs
Time

---
The Assembly Line
Pipelined
Break the job into smaller stages
A
B
C
A
B
C
A
B
C
Jobs
A
B
C
Time

---
Performance Improvements?
Does it take longer to finish each individual job?
Does it take shorter to finish a series of jobs?
What assumptions were made while answering these questions?
Is a 10-stage pipeline better than a 5-stage pipeline?

---
Quantitative Effects
- As a result of pipelining:
  - Time in ns per instruction goes up
  - Each instruction takes more cycles to execute
  - But… average CPI remains roughly the same
  - Clock speed goes up
  - Total execution time goes down, resulting in lower average time per instruction
  - Under ideal conditions, speedup
    = ratio of elapsed times between successive instruction completions
    = number of pipeline stages = increase in clock speed

---
Clocks and Latches
Stage 1
Stage 2

---
Clocks and Latches
Stage 1
L
Stage 2
L
Clk

---
Thank you!

---
AM vs. GM
GM of IPCs = 1 / GM of CPIs
AM of IPCs represents thruput for a workload where each
program runs sequentially for 1 cycle each; but high-IPC
programs contribute more to the AM
GM of IPCs does not represent run-time for any real
workload (what does it mean to multiply instructions?); but
every program’s IPC contributes equally to the final measure

---
Speedup Vs. Percentage
“Speedup” is a ratio = old exec time / new exec time
“Improvement”, “Increase”, “Decrease” usually refer to
percentage relative to the baseline
= (new perf – old perf) / old perf
A program ran in 100 seconds on my old laptop and in 70
seconds on my new laptop
What is the speedup?
What is the percentage increase in performance?
What is the reduction in execution time?