## Slide 1
3810 Review Session
Spring 2023

## Slide 2
Disks Basics
Disk access remains very slow – mechanical head that has to move to the correct “ring” of data – order of milli-seconds – high enough that a context-switch is best
Focus on other metrics, especially reliability
A sector on the disk is associated with a cyclic redundancy code (CRC) – a hash that tells us if the read data is correct or not – it is simply an error detector, not an error corrector
To correct the error, RAID is commonly used
Reliability measures continuous service accomplishment and is usually expressed as mean time to failure (MTTF)
Availability is measured as MTTF/(MTTF+MTTRecovery)

## Slide 3
RAID
RAID 0: no redundancy
RAID 1: mirroring
RAID 2 and 6: memory-style ECC and rarely deployed
RAID 3: bit-interleaved, lower cost, but no query-level parallelism
RAID 4: block-interleaved, lower cost, query-level parallelism, but write bottleneck
RAID 5: block-interleaved, lower cost, query-level parallelism, write parallelism
Parity and XOR!

## Slide 4
Unpipelined processor
CPI:
Clock speed:
Throughput:
Pipelined processor
CPI:
Clock speed:
Throughput:
Circuit Assumptions
Length of full circuit:
Length of each stage:
No hazards
Pipeline Performance

## Slide 5
Data Hazards
No Bypassing
(for the 5-stage pipeline)
Point of production: always RW middle
Point of consumption: always D/R middle
Bypassing
Point of production:
add, sub, etc.: end of ALU
lw: end of DM
Point of consumption:
add, sub, lw: start of ALU
sw $1, 8($2): start of ALU for $2,
start of DM for $1
* PoP
I1 add: IF DR AL DM RW
I2 add: IF DR DR DR AL DM RW
* PoC
* PoP
I1 add: IF DR AL DM RW
I2 add: IF DR AL DM RW
* PoC

## Slide 6
Control Hazards
Assumptions
100 instructions
20 branches
14 Not-Taken, 6 Taken
Branch resolved in 6th cycle (penalty of 5)
Approach 1: Panic and wait
Approach 2: Fetch-next-instr
Approach 3: Branch Delay Slot
Option A: always useful
Option B: useful when the branch
goes along common fork
Option C: useful when the branch
goes along uncommon fork
Option D: no-op, always non-useful
Approach 4: Branch predictor
Accuracy of 90%
Option A
Branch
Slot
NTaken Taken
Option B Option C

## Slide 7
Out of Order Processor
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
T1
T2
T3
T4
T5
T6
Reorder Buffer (ROB)
T1  R1+R2
T2  T1+R3
BEQZ T2
T4  T1+T2
T5  T4+T2
Issue Queue (IQ)
ALU
ALU
ALU
Register File
R1-R32
Results written to
ROB and tags
broadcast to IQ

## Slide 8
Cache Latency
Assumptions
1000 instructions, 1000 cycles, no stalls with L1 hits
# loads/stores:
% of loads/stores that show up at L2:
% of loads/stores that show up at L3:
% of loads/stores that show up at mem:
L2 acc = 10 cyc, L3 acc = 25 cyc, mem acc = 200 cyc

## Slide 9
Cache Size
Assumptions
512KB cache, 8-way set-associative, 64-byte blocks, 32-bit addresses
Data array size = #sets x #ways x blocksize
Tag array size = #sets x #ways x tagsize
Offset bits = log(blocksize)
Index bits = log(#sets)
Tag bits + index bits + offset bits = addresswidth

## Slide 10
Cache Hits/Misses
Assumptions
16 sets, 1 way, 32-byte blocks
Access pattern: 4 40 400 480 512 520 1032 1540
Offset = address % 32 (address modulo 32, extract last 5)
Index = address/32 % 16 (shift right by 5, extract last 4)
Tag = address/512 (shift address right by 9)
32-bit address
23 bits tag 4 bits index 5 bits offset H/M Evicted address
4: 0 0 4 M Inv
40: 0 1 8 M Inv
400: 0 12 16 M Inv
480: 0 15 0 M Inv
512: 1 0 0 M 0
520: 1 0 8 H -
1032: 2 0 8 M 512
1540: 3 0 4 M 1024

## Slide 11
Example 0b
Offset = address % 64 (address modulo 64, extract last 6)
Index = address/64 % 16 (shift right by 6, extract last 4)
Tag = address/1024 (shift address right by 10)
32-bit address
22 bits tag 4 bits index 6 bits offset
8: 0 0 8 M
96: 0 1 32 M
32: 0 0 32 H
480: 0 7 32 M
976: 0 15 16 M
1040: 1 0 16 M
1096: 1 1 8 M
Show how the following addresses map to the cache and yield hits or misses.
The cache is direct-mapped, has 16 sets, and a 64-byte block size.
Addresses: 8, 96, 32, 480, 976, 1040, 1096
.
.
.

## Slide 13
Security
Questions to ask yourself:
How does Meltdown work?
How does Spectre work?
How can you force a footprint? (the relevant code sequence)
How can you examine footprints? (exploiting the side channel)
How can you defend against these attacks?

## Slide 14
Virtual Memory
Questions to ask yourself:
What does the programmer/compiler deal with?
What does the OS deal with?
How is translation done efficiently?

## Slide 15
Synchronization, Consistency
Questions to ask yourself:
Why do multiprocs need to deal with prog. models, coherence, synchronization, consistency?
What are race conditions?
What is an example synchronization primitive and how is it implemented?
What consistency model is assumed by a programmer?
Why is it slow?
How do I make life easier for the programmer and provide high performance?

## Slide 16
GPUs, Disks
Questions to ask yourself:
What are the central philosophies in a GPU?
In what ways does the GPU design differ from a CPU?
What are the different ways that disks provide high reliability?
Can you explain how parity is used to recover lost data?