## Slide 1
Lecture: Out-of-order Processors
Topics: branch predictor wrap-up, a basic out-of-order
processor with issue queue, register renaming,
and reorder buffer

## Slide 2
Tournament Predictors
A local predictor might work well for some branches or
programs, while a global predictor might work well for others
Provide one of each and maintain another predictor to
identify which predictor is best for each branch
Tournament
Predictor
Branch PC
Table of 2-bit
saturating counters
Local
Predictor
Global
Predictor
M
U
X
Alpha 21264:
1K entries in level-1
1K entries in level-2
4K entries
12-bit global history
4K entries
Total capacity: ?

## Slide 3
Branch Target Prediction
In addition to predicting the branch direction, we must
also predict the branch target address
Branch PC indexes into a predictor table; indirect branches
might be problematic
Most common indirect branch: return from a procedure –
can be easily handled with a stack of return addresses

## Slide 4
Problem 1
What is the storage requirement for a global predictor
that uses 3-bit saturating counters and that produces
an index by XOR-ing 12 bits of branch PC with 12 bits
of global history?

## Slide 5
Problem 1
What is the storage requirement for a global predictor
that uses 3-bit saturating counters and that produces
an index by XOR-ing 12 bits of branch PC with 12 bits
of global history?
The index is 12 bits wide, so the table has 2^12 saturating
counters. Each counter is 3 bits wide. So total storage
= 3 * 4096 = 12 Kb or 1.5 KB

## Slide 6
Problem 2
What is the storage requirement for a tournament predictor
that uses the following structures:
  a “selector” that has 4K entries and 2-bit counters
  a “global” predictor that XORs 14 bits of branch PC
  with 14 bits of global history and uses 3-bit counters
  a “local” predictor that uses an 8-bit index into L1, and
  produces a 12-bit index into L2 by XOR-ing branch PC
  and local history. The L2 uses 2-bit counters.

## Slide 7
Problem 2
What is the storage requirement for a tournament predictor
that uses the following structures:
  a “selector” that has 4K entries and 2-bit counters
  a “global” predictor that XORs 14 bits of branch PC
  with 14 bits of global history and uses 3-bit counters
  a “local” predictor that uses an 8-bit index into L1, and
  produces a 12-bit index into L2 by XOR-ing branch PC
  and local history. The L2 uses 2-bit counters.
  Selector = 4K * 2b = 8 Kb
  Global = 3b * 2^14 = 48 Kb
  Local = (12b * 2^8) + (2b * 2^12) = 3 Kb + 8 Kb = 11 Kb
  Total = 67 Kb

## Slide 8
Problem 3
For the code snippet below, estimate the steady-state
bpred accuracies for the default PC+4 prediction, the
1-bit bimodal, 2-bit bimodal, global, and local predictors.
Assume that the global/local preds use 5-bit histories.
do {
for (i=0; i<4; i++) {
increment something
}
for (j=0; j<8; j++) {
increment something
}
k++;
} while (k < some large number)

## Slide 9
Problem 3
For the code snippet below, estimate the steady-state
bpred accuracies for the default PC+4 prediction, the
1-bit bimodal, 2-bit bimodal, global, and local predictors.
Assume that the global/local preds use 5-bit histories.
do {
for (i=0; i<4; i++) {
increment something
}
for (j=0; j<8; j++) {
increment something
}
k++;
} while (k < some large number)
PC+4: 2/13 = 15%
1b Bim: (2+6+1)/(4+8+1)
= 9/13 = 69%
2b Bim: (3+7+1)/13
= 11/13 = 85%
Global: (4+7+1)/13
= 12/13 = 92%
Local: (4+7+1)/13
= 12/13 = 92%

## Slide 10
An Out-of-Order Processor Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
T1
T2
T3
T4
T5
T6
Reorder Buffer (ROB)
T1  R1+R2
T2  T1+R3
BEQZ T2
T4  T1+T2
T5  T4+T2
Issue Queue (IQ)
ALU
ALU
ALU
Register File
R1-R32
Results written to
ROB and tags
broadcast to IQ

## Slide 11
Problem 1
Show the renamed version of the following code:
Assume that you have 4 rename registers T1-T4
R1  R2+R3
R3  R4+R5
BEQZ R1
R1  R1 + R3
R1  R1 + R3
R3  R1 + R3

## Slide 12
Problem 1
Show the renamed version of the following code:
Assume that you have 4 rename registers T1-T4
R1  R2+R3 T1  R2+R3
R3  R4+R5 T2  R4+R5
BEQZ R1 BEQZ T1
R1  R1 + R3 T4  T1+T2
R1  R1 + R3 T1  T4+T2
R3  R1 + R3 T2  T1 +R3

## Slide 13
Design Details - I
Instructions enter the pipeline in order
No need for branch delay slots if prediction happens in time
Instructions leave the pipeline in order – all instructions
that enter also get placed in the ROB – the process of an
instruction leaving the ROB (in order) is called commit –
an instruction commits only if it and all instructions before
it have completed successfully (without an exception)
To preserve precise exceptions, a result is written into the
register file only when the instruction commits – until then,
the result is saved in a temporary register in the ROB

## Slide 14
Design Details - II
Instructions get renamed and placed in the issue queue –
some operands are available (T1-T6; R1-R32), while
others are being produced by instructions in flight (T1-T6)
As instructions finish, they write results into the ROB (T1-T6)
and broadcast the operand tag (T1-T6) to the issue queue –
instructions now know if their operands are ready
When a ready instruction issues, it reads its operands from
T1-T6 and R1-R32 and executes (out-of-order execution)
Can you have WAW or WAR hazards? By using more
names (T1-T6), name dependences can be avoided

## Slide 15
Design Details - III
If instr-3 raises an exception, wait until it reaches the top
of the ROB – at this point, R1-R32 contain results for all
instructions up to instr-3 – save registers, save PC of instr-3,
and service the exception
If branch is a mispredict, flush all instructions after the
branch and start on the correct path – mispredicted instrs
will not have updated registers (the branch cannot commit
until it has completed and the flush happens as soon as the
branch completes)
Potential problems: ?

## Slide 16
Managing Register Names
Logical
Registers
R1-R32
Physical
Registers
P1-P64
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
At the start, R1-R32 can be found in P1-P32
Instructions stop entering the pipeline when P64 is assigned
What happens on commit?
Temporary values are stored in the register file and not the ROB

## Slide 17
The Commit Process
On commit, no copy is required
The register map table is updated – the “committed” value
of R1 is now in P33 and not P1 – on an exception, P33 is
copied to memory and not P1
An instruction in the issue queue need not modify its
input operand when the producer commits
When instruction-1 commits, we no longer have any use
for P1 – it is put in a free pool and a new instruction can
now enter the pipeline  for every instr that commits, a
new instr can enter the pipeline  number of in-flight
instrs is a constant = number of extra (rename) registers

## Slide 18
The Alpha 21264 Out-of-Order Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
Reorder Buffer (ROB)
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
P36  P35+P34
Issue Queue (IQ)
ALU
ALU
ALU
Register File
P1-P64
Results written to
regfile and tags
broadcast to IQ
Speculative
Reg Map
R1P36
R2P34
Committed
Reg Map
R1P1
R2P2