## Slide 1
Lecture: SMT, Cache Hierarchies
Topics: SMT processors, cache access basics/examples

## Slide 2
Thread-Level Parallelism
Motivation:
  a single thread leaves a processor under-utilized
  for most of the time
  by doubling processor area, single thread performance
  barely improves
Strategies for thread-level parallelism:
  multiple threads share the same large processor 
  reduces under-utilization, efficient resource allocation
  Simultaneous Multi-Threading (SMT)
  each thread executes on its own mini processor 
  simple design, low interference between threads
  Chip Multi-Processing (CMP) or multi-core

## Slide 3
How are Resources Shared?
Each box represents an issue slot for a functional unit. Peak thruput is 4 IPC.
Cycles
Superscalar processor has high under-utilization – not enough work every
cycle, especially when there is a cache miss
Fine-grained multithreading can only issue instructions from a single thread
in a cycle – can not find max work every cycle, but cache misses can be tolerated
Simultaneous multithreading can issue instructions from any thread every
cycle – has the highest probability of finding work for every issue slot
Superscalar
Fine-Grained
Multithreading
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Idle

## Slide 4
The Alpha 21264 Out-of-Order Implementation
Branch prediction
and instr fetch
R1  R1+R2
R2  R1+R3
BEQZ R2
R3  R1+R2
R1  R3+R2
Instr Fetch Queue
Decode &
Rename
Instr 1
Instr 2
Instr 3
Instr 4
Instr 5
Instr 6
Reorder Buffer (ROB)
P33  P1+P2
P34  P33+P3
BEQZ P34
P35  P33+P34
P36  P35+P34
Issue Queue (IQ)
ALU
ALU
ALU
Register File
P1-P64
Results written to
regfile and tags
broadcast to IQ
Speculative
Reg Map
R1P36
R2P34
Committed
Reg Map
R1P1
R2P2

## Slide 5
What Resources are Shared?
Multiple threads are simultaneously active (in other words,
a new thread can start without a context switch)
For correctness, each thread needs its own PC, IFQ,
logical regs (and its own mappings from logical to phys regs)
For performance, each thread could have its own ROB/LSQ
(so that a stall in one thread does not stall commit in other
threads), I-cache, branch predictor, D-cache, etc. (for low
interference), although note that more sharing  better
utilization of resources
Each additional thread costs a PC, IFQ, rename tables,
and ROB – cheap!

## Slide 6
Front
End
Front
End
Front
End
Front
End
Execution Engine
Rename
ROB
I-Cache
Bpred
Regs
IQ
FUs
DCache
Private/
Shared
Front-end
Private
Front-end
Shared
Exec Engine
Pipeline Structure

## Slide 7
Resource Sharing
R1  R1 + R2
R3  R1 + R4
R5  R1 + R3
R2  R1 + R2
R5  R1 + R2
R3  R5 + R3
P65 P1 + P2
P66  P65 + P4
P67  P65 + P66
P76  P33 + P34
P77  P33 + P76
P78  P77 + P35
P65 P1 + P2
P66  P65 + P4
P67  P65 + P66
P76  P33 + P34
P77  P33 + P76
P78  P77 + P35
FU
FU
FU
FU
Instr Fetch
Instr Fetch
Instr Rename
Instr Rename
Issue Queue
Register File
Thread-1
Thread-2

## Slide 8
Performance Implications of SMT
Single thread performance is likely to go down (caches,
branch predictors, registers, etc. are shared) – this effect
can be mitigated by trying to prioritize one thread
While fetching instructions, thread priority can dramatically
influence total throughput – a widely accepted heuristic
(ICOUNT): fetch such that each thread has an equal share
of processor resources
With eight threads in a processor with many resources,
SMT yields throughput improvements of roughly 2-4

## Slide 9
Multi-Programmed Speedup
sixtrack and eon do not degrade
their partners (small working sets?)
swim and art degrade their
partners (cache contention?)
Best combination: swim & sixtrack
worst combination: swim & art
Static partitioning ensures low
interference – worst slowdown
is 0.9

## Slide 10
The Cache Hierarchy
Core
L1
L2
L3
Off-chip memory

## Slide 11
Problem 1
Memory access time: Assume a program that has cache
access times of 1-cyc (L1), 10-cyc (L2), 30-cyc (L3), and
300-cyc (memory), and MPKIs of 20 (L1), 10 (L2), and 5 (L3).
Should you get rid of the L3?

## Slide 12
Problem 1
Memory access time: Assume a program that has cache
access times of 1-cyc (L1), 10-cyc (L2), 30-cyc (L3), and
300-cyc (memory), and MPKIs of 20 (L1), 10 (L2), and 5 (L3).
Should you get rid of the L3?
With L3: 1000 + 10x20 + 30x10 + 300x5 = 3000
Without L3: 1000 + 10x20 + 10x300 = 4200

## Slide 14
Accessing the Cache
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
8 words: 3 index bits
Byte address
Data array
Sets
Offset

## Slide 15
The Tag Array
8-byte words
101000
Direct-mapped cache:
each address maps to
a unique address
Byte address
Tag
Compare
Data array
Tag array

## Slide 16
Increasing Line Size
32-byte cache
line size or
block size
10100000
Byte address
Tag
Data array
Tag array
Offset
A large cache line size  smaller tag array,
fewer misses because of spatial locality

## Slide 17
Associativity
10100000
Byte address
Tag
Data array
Tag array
Set associativity  fewer conflicts; wasted power
because multiple data and tags are read
Way-1
Way-2
Compare

## Slide 18
Problem 2
Assume a direct-mapped cache with just 4 sets. Assume
that block A maps to set 0, B to 1, C to 2, D to 3, E to 0, and
so on. For the following access pattern, estimate the hits
and misses:
A B B E C C A D B F A E G C G A

## Slide 19
Problem 2
Assume a direct-mapped cache with just 4 sets. Assume
that block A maps to set 0, B to 1, C to 2, D to 3, E to 0, and
so on. For the following access pattern, estimate the hits
and misses:
A B B E C C A D B F A E G C G A
M MH MM H MM HM HMM M M M

## Slide 20
Problem 3
Assume a 2-way set-associative cache with just 2 sets.
Assume that block A maps to set 0, B to 1, C to 0, D to 1,
E to 0, and so on. For the following access pattern,
estimate the hits and misses:
A B B E C C A D B F A E G C G A

## Slide 21
Problem 3
Assume a 2-way set-associative cache with just 2 sets.
Assume that block A maps to set 0, B to 1, C to 0, D to 1,
E to 0, and so on. For the following access pattern,
estimate the hits and misses:
A B B E C C A D B F A E G C G A
M MH M MH MM HM HMM M H M

## Slide 22
Problem 4
64 KB 16-way set-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets?
How many index bits, offset bits, tag bits?
How large is the tag array?

## Slide 23
Problem 4
64 KB 16-way set-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets? 64
How many index bits (6), offset bits (6), tag bits (28)?
How large is the tag array (28 Kb)?

## Slide 24
Problem 5
8 KB fully-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets? How many ways?
How many index bits, offset bits, tag bits?
How large is the tag array?

## Slide 25
Problem 5
8 KB fully-associative data cache array with 64
byte line sizes, assume a 40-bit address
How many sets (1) ? How many ways (128) ?
How many index bits (0), offset bits (6), tag bits (34) ?
How large is the tag array (544 bytes) ?

## Slide 26
Types of Cache Misses
Compulsory misses: happens the first time a memory
word is accessed – the misses for an infinite cache
Capacity misses: happens because the program touched
many other words before re-touching the same word – the
misses for a fully-associative cache
Conflict misses: happens because two words map to the
same location in the cache – the misses generated while
moving from a fully-associative to a direct-mapped cache
Sidenote: can a fully-associative cache have more misses
than a direct-mapped cache of the same size?