## Slide 1
Lecture: Memory Basics and Innovations
Topics: memory organization basics, memory scheduling policies

## Slide 2
DRAM Main Memory
Main memory is stored in DRAM cells that have much
higher storage density
DRAM cells lose their state over time – must be refreshed
periodically, hence the name Dynamic
DRAM access suffers from long access time and high
energy overhead

## Slide 3
Memory Architecture
Processor
Memory Controller
Address/Cmd
Data
DIMM
Bank
Row Buffer
DIMM: a PCB with DRAM chips on the back and front
Rank: a collection of DRAM chips that work together to respond to a
request and keep the data bus full
A 64-bit data bus will need 8 x8 DRAM chips or 4 x16 DRAM chips or..
Bank: a subset of a rank that is busy during one request
Row buffer: the last row (say, 8 KB) read from a bank, acts like a cache

## Slide 4
DRAM Array Access
16Mb DRAM array = 4096 x 4096 array of bits
12 row address bits
arrive first
Column decoder
12 column address bits
arrive next
Some bits
returned to CPU
4096 bits
are read out
Row Access Strobe (RAS)
Column Access Strobe (CAS)
Row Buffer

## Slide 5
Organizing a Rank
DIMM, rank, bank, array  form a hierarchy in the
storage organization
Because of electrical constraints, only a few DIMMs can
be attached to a bus
One DIMM can have 1-4 ranks
For energy efficiency, use wide-output DRAM chips – better
to activate only 4 x16 chips per request than 16 x4 chips
For high capacity, use narrow-output DRAM chips – since the
ranks on a channel are limited, capacity per rank is boosted
by having 16 x4 2Gb chips than 4 x16 2Gb chips

## Slide 6
Organizing Banks and Arrays
A rank is split into many banks (8-16) to boost parallelism
within a rank
Ranks and banks offer memory-level parallelism
A bank is made up of multiple arrays (subarrays, tiles, mats)
To maximize density, arrays within a bank are made large
 rows are wide  row buffers are wide (e.g., 8KB read for
a 64B request, called overfetch)

## Slide 7
Problem 1
What is the maximum memory capacity supported by the
following server: 2 processor sockets, each socket has
4 memory channels, each channel supports 2 dual-ranked
DIMMs, and x4 4Gb DRAM chips?
What is the memory bandwidth available to the server if
each memory channel runs at 800 MHz?

## Slide 8
Problem 1
What is the maximum memory capacity supported by the
following server: 2 processor sockets, each socket has
4 memory channels, each channel supports 2 dual-ranked
DIMMs, and x4 4Gb DRAM chips?
2 sockets x 4 channels x 2 DIMMs x 2 ranks x
16 chips x 4Gb capacity = 256 GB
What is the memory bandwidth available to the server if
each memory channel runs at 800 MHz?
2 sockets x 4 channels x 800M (cycles per second) x
2 (DDR, hence 2 transfers per cycle) x 64 (bits per transfer)
= 102.4 GB/s

## Slide 9
Problem 2
A basic memory mat has 512 rows and 512 columns. What
is the memory chip capacity if there are 512 mats in a bank,
and 8 banks in a chip?

## Slide 10
Problem 2
A basic memory mat has 512 rows and 512 columns. What
is the memory chip capacity if there are 512 mats in a bank,
and 8 banks in a chip?
Memory chip capacity = 512 rows x 512 cols x
512 mats x 8 banks = 1 Gb

## Slide 11
Row Buffers
Each bank has a single row buffer
Row buffers act as a cache within DRAM
  Row buffer hit: ~20 ns access time (must only move
  data from row buffer to pins)
  Empty row buffer access: ~40 ns (must first read
  arrays, then move data from row buffer to pins)
  Row buffer conflict: ~60 ns (must first precharge the
  bitlines, then read new row, then move data to pins)
In addition, must wait in the queue (tens of nano-seconds)
and incur address/cmd/data transfer delays (~10 ns)

## Slide 12
Open/Closed Page Policies
If an access stream has locality, a row buffer is kept open
  Row buffer hits are cheap (open-page policy)
  Row buffer miss is a bank conflict and expensive
  because precharge is on the critical path
If an access stream has little locality, bitlines are precharged
immediately after access (close-page policy)
  Nearly every access is a row buffer miss
  The precharge is usually not on the critical path
Modern memory controller policies lie somewhere between
these two extremes (usually proprietary)

## Slide 13
Problem 3
For the following access stream, estimate the finish times for
each access with the following scheduling policies:
Req Time of arrival Open Closed Oracular
X 0 ns
Y 10 ns
X+1 100 ns
X+2 200 ns
Y+1 250 ns
X+3 300 ns
Note that X, X+1, X+2, X+3 map to the same row and Y, Y+1
map to a different row in the same bank. Ignore bus and
queuing latencies. The bank is precharged at the start.

## Slide 14
Problem 3
For the following access stream, estimate the finish times for
each access with the following scheduling policies:
Req Time of arrival Open Closed Oracular
X 0 ns 40 40 40
Y 10 ns 100 100 100
X+1 100 ns 160 160 160
X+2 200 ns 220 240 220
Y+1 250 ns 310 300 290
X+3 300 ns 370 360 350
Note that X, X+1, X+2, X+3 map to the same row and Y, Y+1
map to a different row in the same bank. Ignore bus and
queuing latencies. The bank is precharged at the start.

## Slide 15
Problem 4
For the following access stream, estimate the finish times for
each access with the following scheduling policies:
Req Time of arrival Open Closed Oracular
X 10 ns
X+1 15 ns
Y 100 ns
Y+1 180 ns
X+2 190 ns
Y+2 205 ns
Note that X, X+1, X+2, X+3 map to the same row and Y, Y+1
map to a different row in the same bank. Ignore bus and
queuing latencies. The bank is precharged at the start.

## Slide 16
Problem 4
For the following access stream, estimate the finish times for
each access with the following scheduling policies:
Req Time of arrival Open Closed Oracular
X 10 ns 50 50 50
X+1 15 ns 70 70 70
Y 100 ns 160 140 140
Y+1 180 ns 200 220 200
X+2 190 ns 260 300 260
Y+2 205 ns 320 240 320
Note that X, X+1, X+2, X+3 map to the same row and Y, Y+1
map to a different row in the same bank. Ignore bus and
queuing latencies. The bank is precharged at the start.
** A more sophisticated oracle can do even better.

## Slide 17
Address Mapping Policies
Consecutive cache lines can be placed in the same row
to boost row buffer hit rates
Consecutive cache lines can be placed in different ranks
to boost parallelism
Example address mapping policies:
row:rank:bank:channel:column:blkoffset
row:column:rank:bank:channel:blkoffset

## Slide 18
Reads and Writes
A single bus is used for reads and writes
The bus direction must be reversed when switching between
reads and writes; this takes time and leads to bus idling
Hence, writes are performed in bursts; a write buffer stores
pending writes until a high water mark is reached
Writes are drained until a low water mark is reached

## Slide 19
Scheduling Policies
FCFS: Issue the first read or write in the queue that is
ready for issue
First Ready - FCFS: First issue row buffer hits if you can
Close page -- early precharge
Stall Time Fair: First issue row buffer hits, unless other
threads are being neglected

## Slide 20
Error Correction
For every 64-bit word, can add an 8-bit code that can
detect two errors and correct one error; referred to as
SECDED – single error correct double error detect
A rank is now made up of 9 x8 chips, instead of 8 x8 chips
Stronger forms of error protection exist: a system is
chipkill correct if it can handle an entire DRAM chip failure