## Slide 1
Lecture: Pipelining Hazards
Topics: structural and data hazards
HW2 posted later today; due in a week

## Slide 2
A 5-Stage Pipeline
Source: H&P textbook

## Slide 3
A 5-Stage Pipeline
Use the PC to access the I-cache and increment PC by 4

## Slide 4
A 5-Stage Pipeline
Read registers, compare registers, compute branch target; for now, assume
branches take 2 cyc (there is enough work that branches can easily take more)

## Slide 5
A 5-Stage Pipeline
ALU computation, effective address computation for load/store

## Slide 6
A 5-Stage Pipeline
Memory access to/from data cache, stores finish in 4 cycles

## Slide 7
A 5-Stage Pipeline
Write result of ALU computation or load into register file

## Slide 8
RISC/CISC Loads/Stores
Registers and memory
Complex and reduced instrs
Format of a load/store

## Slide 9
Problem 3
Convert this C code into equivalent RISC assembly
instructions
a[i] = b[i] + c[i];

## Slide 10
Problem 3
Convert this C code into equivalent RISC assembly
instructions
a[i] = b[i] + c[i];
LD R2, [R1] # R1 has the address for variable i
MUL R3, R2, 8 # the offset from the start of the array
ADD R7, R3, R4 # R4 has the address of a[0]
ADD R8, R3, R5 # R5 has the address of b[0]
ADD R9, R3, R6 # R6 has the address of c[0]
LD R10, [R8] # Bringing b[i]
LD R11, [R9] # Bringing c[i]
ADD R12, R11, R10 # Sum is in R12
ST R12, [R7] # Putting result in a[i]

## Slide 11
Pipeline Summary
RR ALU DM RW
ADD R3  R1, R2 Rd R1,R2 R1+R2 -- Wr R3
BEZ R1, [R5] Rd R1, R5 -- -- --
Compare, Set PC
LD R6  8[R3] Rd R3 R3+8 Get data Wr R6
ST R6  8[R3] Rd R3,R6 R3+8 Wr data --

## Slide 12
Problem 4
For the following code sequence, show how the instrs
flow through the pipeline:
ADD R3  R1, R2
LD R7  8[R6]
ST R9  4[R8]
BEZ R4, [R5]

## Slide 13
Problem 4
For the following code sequence, show how the instrs
flow through the pipeline:
ADD R3  R1, R2
LD R7  8[R6]
ST R9  4[R8]
BEZ R4, [R5]
ADD
ADD
ADD
ADD
ADD
BEZ
BEZ
ST
ST
ST
ST
LD
LD
LD
LD
LD

## Slide 14
Hazards
Structural hazards: different instructions in different stages
(or the same stage) conflicting for the same resource
Data hazards: an instruction cannot continue because it
needs a value that has not yet been generated by an
earlier instruction
Control hazard: fetch cannot continue because it does
not know the outcome of an earlier branch – special case
of a data hazard – separate category because they are
treated in different ways

## Slide 15
Structural Hazards
Example: a unified instruction and data cache 
stage 4 (MEM) and stage 1 (IF) can never coincide
The later instruction and all its successors are delayed
until a cycle is found when the resource is free  these
are pipeline bubbles
Structural hazards are easy to eliminate – increase the
number of resources (for example, implement a separate
instruction and data cache)

## Slide 16
Problem 5
D/R
ALU
DM
RW
IF
CYC-1
D/R
ALU
DM
RW
IF
CYC-2
D/R
ALU
DM
RW
IF
CYC-3
D/R
ALU
DM
RW
IF
CYC-4
D/R
ALU
DM
RW
IF
CYC-5
D/R
ALU
DM
RW
IF
CYC-6
D/R
ALU
DM
RW
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
Show the instruction occupying each stage in each cycle (no bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R7+R8R9

## Slide 17
Problem 5
D/R
ALU
DM
RW
IF
I1
CYC-1
D/R
I1
ALU
DM
RW
IF
I2
CYC-2
D/R
I2
ALU
I1
DM
RW
IF
I3
CYC-3
D/R
I2
ALU
DM
I1
RW
IF
I3
CYC-4
D/R
I2
ALU
DM
RW
I1
IF
I3
CYC-5
D/R
I3
ALU
I2
DM
RW
IF
I4
CYC-6
D/R
I4
ALU
I3
DM
I2
RW
IF
I5
CYC-7
D/R
ALU
DM
I3
RW
I2
IF
CYC-8
Show the instruction occupying each stage in each cycle (no bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R7+R8R9

## Slide 18
Bypassing: 5-Stage Pipeline
Source: H&P textbook

## Slide 19
Problem 6
D/R
ALU
DM
RW
IF
CYC-1
D/R
ALU
DM
RW
IF
CYC-2
D/R
ALU
DM
RW
IF
CYC-3
D/R
ALU
DM
RW
IF
CYC-4
D/R
ALU
DM
RW
IF
CYC-5
D/R
ALU
DM
RW
IF
CYC-6
D/R
ALU
DM
RW
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
Show the instruction occupying each stage in each cycle (with bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R3+R8R9.
Identify the input latch for each input operand.

## Slide 20
Problem 6
Show the instruction occupying each stage in each cycle (with bypassing)
if I1 is R1+R2R3 and I2 is R3+R4R5 and I3 is R3+R8R9.
Identify the input latch for each input operand.
D/R
ALU
DM
RW
IF
I1
CYC-1
D/R
I1
ALU
DM
RW
IF
I2
CYC-2
D/R
I2
ALU
I1
DM
RW
IF
I3
CYC-3
D/R
I3
ALU
I2
DM
I1
RW
IF
I4
CYC-4
D/R
I4
ALU
I3
DM
I2
RW
I1
IF
I5
CYC-5
D/R
ALU
DM
I3
RW
I2
IF
CYC-6
D/R
ALU
DM
RW
I3
IF
CYC-7
D/R
ALU
DM
RW
IF
CYC-8
L3 L3 L4 L3 L5 L3