## Slide 1
Lecture: Branch Prediction
Topics: dynamic branch prediction,
bimodal/global/local/tournament predictors
(Chapter 3, notes on class webpage)

## Slide 2
Software Pipelining
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
Loop: S.D F4, 16(R1)
ADD.D F4, F0, F2
L.D F0, 0(R1)
DADDUI R1, R1,# -8
BNE R1, R2, Loop
Advantages: achieves nearly the same effect as loop unrolling, but
without the code expansion – an unrolled loop may have inefficiencies
at the start and end of each iteration, while a sw-pipelined loop is
almost always in steady state – a sw-pipelined loop can also be unrolled
to reduce loop overhead
Disadvantages: does not reduce loop overhead, may require more
registers

## Slide 3
Problem 4
for (i=1000; i>0; i--)
x[i] = y[i] * s;
Loop: L.D F0, 0(R1) ; F0 = array element
MUL.D F4, F0, F2 ; multiply scalar
S.D F4, 0(R2) ; store result
DADDUI R1, R1,# -8 ; decrement address pointer
DADDUI R2, R2,#-8 ; decrement address pointer
BNE R1, R3, Loop ; branch if R1 != R3
NOP
Source code
Assembly code
LD -> any : 1 stall
FPMUL -> any: 5 stalls
FPMUL -> ST : 4 stalls
IntALU -> BR : 1 stall
Show the SW pipelined version of the code and does it cause stalls?
Loop: S.D F4, 0(R2)
MUL F4, F0, F2
L.D F0, 0(R1)
DADDUI R2, R2, #-8
BNE R1, R3, Loop
DADDUI R1, R1, #-8 There will be no stalls

## Slide 4
Software Pipelining Reminders
Note how the store instruction needs an offset in some cases
Easiest to use more register names to avoid artificial dependences
LD R1 
ADD R1  R1
SD R1  [ ]
SD R1 
ADD R1  R1
LD R1 
LD R1 
ADD R2  R1
SD R2  [ ]
SD R2 
ADD R2  R1
LD R1 

## Slide 5
Static vs. Dynamic
Predication and speculation are other compiler techniques needed
to increase performance
To get high performance with a compiler-based approach,
we need support for predication, tables to analyze
dependences, etc. Plus, scheduling goes haywire if there
are cache misses.
Difficult to achieve the highest performance with a purely
static (compiler-based) approach – it continues to have value
for highly simple in-order processors
For highest performance, dynamic/hardware approaches are
most effective, and the compiler can help such processors too

## Slide 6
Amdahl’s Law
Architecture design is very bottleneck-driven – make the
common case fast, do not waste resources on a component
that has little impact on overall performance/power
Amdahl’s Law: performance improvements through an
enhancement is limited by the fraction of time the
enhancement comes into play
Example: a web server spends 40% of time in the CPU
and 60% of time doing I/O – a new processor that is ten
times faster results in a 36% reduction in execution time
(speedup of 1.56) – Amdahl’s Law states that maximum
execution time reduction is 40% (max speedup of 1.66)

## Slide 7
Principle of Locality
Most programs are predictable in terms of instructions
executed and data accessed
The 90-10 Rule: a program spends 90% of its execution
time in only 10% of the code
Temporal locality: a program will shortly re-visit X
Spatial locality: a program will shortly visit X+1

## Slide 8
Pipeline without Branch Predictor
IF (br)
PC
Reg Read
Compare
Br-target
PC + 4
In the 5-stage pipeline, a branch completes in two cycles 
If the branch went the wrong way, one incorrect instr is fetched 
One stall cycle per incorrect branch

## Slide 9
Pipeline with Branch Predictor
IF (br)
PC
Reg Read
Compare
Br-target
In the 5-stage pipeline, a branch completes in two cycles 
If the branch went the wrong way, one incorrect instr is fetched 
One stall cycle per incorrect branch
Branch
Predictor

## Slide 10
1-Bit Bimodal Prediction
For each branch, keep track of what happened last time
and use that outcome as the prediction
What are prediction accuracies for branches 1 and 2 below:
while (1) {
for (i=0;i<10;i++) { branch-1
…
}
for (j=0;j<20;j++) { branch-2
…
}
}

## Slide 11
2-Bit Bimodal Prediction
For each branch, maintain a 2-bit saturating counter:
if the branch is taken: counter = min(3,counter+1)
if the branch is not taken: counter = max(0,counter-1)
If (counter >= 2), predict taken, else predict not taken
Advantage: a few atypical branches will not influence the
prediction (a better measure of “the common case”)
Especially useful when multiple branches share the same
counter (some bits of the branch PC are used to index
into the branch predictor)
Can be easily extended to N-bits (in most processors, N=2)

## Slide 12
Bimodal 1-Bit Predictor
Branch PC
10 bits
Table of
1K entries
Each
entry is
a bit
The table keeps track of what the branch did last time

## Slide 13
Bimodal 2-Bit Predictor
Branch PC
10 bits
Table of
1K entries
Each
entry is
a 2-bit
sat.
counter
The table keeps track of the common-case
outcome for the branch

## Slide 14
Correlating Predictors
Basic branch prediction: maintain a 2-bit saturating
counter for each entry (or use 10 branch PC bits to index
into one of 1024 counters) – captures the recent
“common case” for each branch
Can we take advantage of additional information?
  If a branch recently went 01111, expect 0; if it
  recently went 11101, expect 1; can we have a
  separate counter for each case?
  If the previous branches went 01, expect 0; if the
  previous branches went 11, expect 1; can we have
  a separate counter for each case?
  Hence, build correlating predictors

## Slide 15
Global Predictor
Branch PC
10 bits
Table of
16K entries
Each
entry is
a 2-bit
sat.
counter
The table keeps track of the common-case
outcome for the branch/history combo
Global history
CAT or XOR

## Slide 16
Local Predictor
Branch PC
Table of
16K entries
of 2-bit
saturating
counters
Table of 64 entries of 14-bit
histories for a single branch
10110111011001
Use 6 bits of branch PC to
index into local history table
14-bit history
indexes into
next level
Also a two-level predictor that only
uses local histories at the first level

## Slide 17
Local Predictor
Branch PC
6 bits
Table of
1K entries
Each
entry is
a 2-bit
sat.
counter
The table keeps track of the common-case
outcome for the branch/local-history combo
Local history
10 bit entries
XOR
64 entries
10 bits

## Slide 18
Local/Global Predictors
Instead of maintaining a counter for each branch to
capture the common case,
Maintain a counter for each branch and surrounding pattern
If the surrounding pattern belongs to the branch being
predicted, the predictor is referred to as a local predictor
If the surrounding pattern includes neighboring branches,
the predictor is referred to as a global predictor

## Slide 19
Tournament Predictors
A local predictor might work well for some branches or
programs, while a global predictor might work well for others
Provide one of each and maintain another predictor to
identify which predictor is best for each branch
Tournament
Predictor
Branch PC
Table of 2-bit
saturating counters
Local
Predictor
Global
Predictor
M
U
X
Alpha 21264:
1K entries in level-1
1K entries in level-2
4K entries
12-bit global history
4K entries
Total capacity: ?

## Slide 20
Branch Target Prediction
In addition to predicting the branch direction, we must
also predict the branch target address
Branch PC indexes into a predictor table; indirect branches
might be problematic
Most common indirect branch: return from a procedure –
can be easily handled with a stack of return addresses

## Slide 21
Problem 1
What is the storage requirement for a global predictor
that uses 3-bit saturating counters and that produces
an index by XOR-ing 12 bits of branch PC with 12 bits
of global history?

## Slide 22
Problem 1
What is the storage requirement for a global predictor
that uses 3-bit saturating counters and that produces
an index by XOR-ing 12 bits of branch PC with 12 bits
of global history?
The index is 12 bits wide, so the table has 2^12 saturating
counters. Each counter is 3 bits wide. So total storage
= 3 * 4096 = 12 Kb or 1.5 KB

## Slide 23
Problem 2
What is the storage requirement for a tournament predictor
that uses the following structures:
  a “selector” that has 4K entries and 2-bit counters
  a “global” predictor that XORs 14 bits of branch PC
  with 14 bits of global history and uses 3-bit counters
  a “local” predictor that uses an 8-bit index into L1, and
  produces a 12-bit index into L2 by XOR-ing branch PC
  and local history. The L2 uses 2-bit counters.

## Slide 24
Problem 2
What is the storage requirement for a tournament predictor
that uses the following structures:
  a “selector” that has 4K entries and 2-bit counters
  a “global” predictor that XORs 14 bits of branch PC
  with 14 bits of global history and uses 3-bit counters
  a “local” predictor that uses an 8-bit index into L1, and
  produces a 12-bit index into L2 by XOR-ing branch PC
  and local history. The L2 uses 2-bit counters.
  Selector = 4K * 2b = 8 Kb
  Global = 3b * 2^14 = 48 Kb
  Local = (12b * 2^8) + (2b * 2^12) = 3 Kb + 8 Kb = 11 Kb
  Total = 67 Kb

## Slide 25
Problem 3
For the code snippet below, estimate the steady-state
bpred accuracies for the default PC+4 prediction, the
1-bit bimodal, 2-bit bimodal, global, and local predictors.
Assume that the global/local preds use 5-bit histories.
do {
for (i=0; i<4; i++) {
increment something
}
for (j=0; j<8; j++) {
increment something
}
k++;
} while (k < some large number)

## Slide 26
Problem 3
For the code snippet below, estimate the steady-state
bpred accuracies for the default PC+4 prediction, the
1-bit bimodal, 2-bit bimodal, global, and local predictors.
Assume that the global/local preds use 5-bit histories.
do {
for (i=0; i<4; i++) {
increment something
}
for (j=0; j<8; j++) {
increment something
}
k++;
} while (k < some large number)
PC+4: 2/13 = 15%
1b Bim: (2+6+1)/(4+8+1)
= 9/13 = 69%
2b Bim: (3+7+1)/13
= 11/13 = 85%
Global: (4+7+1)/13
= 12/13 = 92%
Local: (4+7+1)/13
= 12/13 = 92%