## Slide 1
Lecture: Self-Driving Cars
Topics: System analysis for two systems: with and
without LIDAR
Email me to communicate team/project and set up
meeting times

## Slide 2
Self-Driving Cars Intro
Several players: Waymo, Tesla, Mobileye, Uber, NVIDIA
Xavier SoC, Audi zFAS board
Level 2 autonomy: car handles steering/accel in limited
conditions, (alert) driver handles rest (hands-off)
Level 3 autonomy: car handles everything in limited
conditions, driver serves as back-up (eyes-off)
Level 4 autonomy: driver helps only when entering
unmapped areas or during severe weather (mind-off)
Level 5 autonomy: no steering wheel

## Slide 3
LIDAR vs. No-LIDAR
LIDAR is very expensive ($75K); hence, Tesla and Mobileye
are focusing on vision-based solutions
Recent announcements claim that top-of-the-line LIDAR
may cost $7,500, with short-range LIDAR being under $5K
https://techcrunch.com/2019/03/06/waymo-to-start-selling-standalone-lidar-sensors/
As we’ll see, LIDAR has other latency problems

## Slide 4
Self-Driving Car Pipeline (Vision-Based)
Need decimeter-level accuracy for localization; GPS fails; localizer
gives them centimeter-level accuracy
Need a locally stored map (41 TB for USA)

## Slide 5
Metrics
99.99th percentile tail latency of 100ms would be faster
than fastest human reaction times (target supported by
industry, but will likely be a moving target); 10 frames/sec
Power and cooling (need cooling because the computers
will be inside the cabin); 77W cooling for every 100W
dissipated; a 400W computer reduces MPG by 1; a
CPU+3GPU system (~1000W) lowers driving range by 6%
(and 11.5% once you add storage+cooling)
Also need high storage and reliability (recall that Tesla FSD
executes every computation twice)

## Slide 6
Algorithms
Object detection: YOLO; DNN based
Object tracker: GOTURN; DNN based and a few
book-keeping tables
Localization: ORB-Slam; lots of trigonometric calculations
Motion and Mission planning: MOTPLAN and MISPLAN
from Autoware

## Slide 7
Bottleneck Analysis
DNNs implemented with Eyeriss and EIE

## Slide 8
Localization

## Slide 9
Feature Extraction
Ops in feature detector
not clear.
Rest are trig ops that
are implemented with
LUTs

## Slide 10
Results
Power for a single camera
(Tesla has 8)
For the whole system, GPU
lowers driving range by 12%
and ASICs by 2%

## Slide 11
Scalability Results
VGG accuracy improves from 80% to 87% when resolution is doubled
Not clear how the bottlenecks change (compute, memory, reuse patterns)

## Slide 12
Summary
Detection, Localization, Tracking, Planning are major steps
The first three take up 94% of compute
Contributions: a pipeline with publicly available frameworks,
bottleneck analysis, acceleration with GPU/FPGA/ASIC
GPUs and ASIC offer two orders of magnitude speedup,
but GPUs consume too much power
More work remains – lower latency, lower power, higher
resolution, feature extraction, other bottlenecks

## Slide 13
LIDAR-based Approach [Zhao et al.]
Joint work with Pony.AI; characterization based on several
hours of driving on their test fleet over 3 months
They rely on LIDAR and their software pipeline has
relatively little DNN

## Slide 14
Software Pipeline

## Slide 15
LIDAR Pipeline
Several steps, with segmentation
being a major overhead
Segmentation extracts useful
semantic info (relevant objects)
from the background
The latency is worse when there
are more nearby objects, since
there are more reflected points
to deal with
This leads to high variance,
especially when collisions are
more likely

## Slide 16
LIDAR Perception Latency
Max time is a relevant metric because it disproportionately
impacts safety
They observe that long LIDAR perception latency also
disproportionately impacts overall latency
(The LIDAR sampling rate is 100ms)

## Slide 17
Safety Score
They compute a safety score that factors in the response
time along with velocity/acceleration
They design a predictor to estimate response time based
on the count/proximity of objects in the scene and how
hardware resources (CPU/GPU) are allocated to each part
of the software pipeline

## Slide 18
References
“The Architectural Implications of Autonomous Driving: Constraints
and Acceleration”, S.-C. Lin et al., ASPLOS 2018
“Towards Safety Aware Computing System Design in Autonomous
Vehicles”, Zhao et al., Arxiv, 2019
“Driving into the Memory Wall”, Jung et al., MemSys 2018